In quality mode for a certain colour i the brightness Bi of a scan can be described as a function of gain gi and exposure time ti (equatioin I). The constants ai and ci have to be provided or determined.
(I)	B_{i} = a_{i} cdot func e^{c_{i} cdot g^{2}_{i}} cdot t_{i}
This also applies to the mean brightnesses Bi0 of the calibration lines, where the values for gain gi0 and exposure time ti0 are provided by the d7_Calibration_Read.
B_{i0} = a_{i} cdot func e^{c_{i} cdot g^{2}_{i0}} cdot t_{i0}
Solving this equation for ai leads to equation II.
(II)	a_{i} = {B_{i0}} over {t_{i0}} cdot func e^{-c_{i} cdot g^{2}_{i0} }

Thus in quality mode calibration can be done with the following expression (III).
(III)	{B_{i}} over {B_{i0}} = func e^{c_{i} cdot (g^{2}_{i} - g^{2}_{io} ) } cdot {t_{i}} over {t_{i0}}
Here the overall correction factor F = Bi/Bi0 is the product of a gain part G(gi, gi0) and a time part H(t0,ti0). In quality mode the strategy is to do most calibration by exposure time. So let us determine that G = F^(1/p) and H = F^((p-1)/p) where p is around 10. From the data obtained from listening to the Windows programs there is no indication that they would change gain in order to calibrate. So we may end up settting G = 1 and do everything with exposure time.

Normal mode uses higher gains and shorter exposure times. The relation between brightness Bi, gain gi and exposure time ti can be described with the introduction of offset factors ni which have to be provided, i.e. experimentally determined.
B_{i} = n_{i} cdot a_{i} cdot func e^{c_{i} cdot g_{i}^{2} } cdot t_{i} - (n_{i} - 1 ) cdot 65536
Using (II) from the calibration this leads to IV.
(IV)	B_{i} = n_{i} cdot {B_{i0}} over {t_{i0}} cdot func e^{c_{i} cdot (g^{2}_{i} - g^{2}_{i0} ) } cdot t_{i} - (n_{i} - 1 ) cdot 65536
Strategy for normal mode is to first use default exposure times ti to calculate the gain for the Brightness Bi to be reached.
g_{i} = sqrt{{1} over {c_{i}} cdot ln({(B_{i} + ({n_{i} - 1 }) cdot 65536 ) cdot t_{i0} } over {n_{i} cdot B_{i0} cdot t_{i} } ) + g_{i0}^{2} }
Then the gains are corrected for constraints and final exposure times are calculated using IV.
t_{i} = {(B_{i} + (n_{i} - 1 ) cdot 65536 ) cdot t_{i0} } over {n_{i} cdot B_{i0} } cdot func e^{c_{i} cdot (g^{2}_{i0} - g^{2}_{i} ) }
For the ProScan 7200 this frequently results in constraint violation for the ti of single colour planes and therefore in tinted scans which will need further correction.